## Slide 1: A Secure Framework for Monitoring Operating Systems Using SPEs in Cell/B.E.
Kenichi Kourai (Kyushu Institute of Technology)
Takuya Nagata (Kyushu Institute of Technology)
Notes: I'm Kenichi Kourai from Kyushu Institute of Technology.
Today, I'd like to talk about "a secure framework for monitoring operating systems using SPEs in Cell/B.E."

## Slide 2: Attacks against OSes
OSes are not an exception of attacks
  e.g. kernel rootkits
  All the applications are also compromised if the OS is compromised
It is necessary to check the integrity of OSes
  Not only at the boot time, but also at runtime
    OSes are long-running software
  This can increase the reliability of the system
kernel
rootkit
OS
application
application
Notes: In recent years, computer systems suffer from various attacks from the Internet.
Operating systems are not an exception of such attacks.
For example, many kernel rootkits have been found.
Kernel rootkits modify a part of the OS and change its behavior.
If the OS is compromised, all the applications on top of it are also compromised because they strongly depend on the functions provided by the OS.
To increase the reliability of the system, it is necessary to check the integrity of OSes, not only at the boot time, but also at runtime.
This is because OSes are long-running software.
Even if the OS is not compromised when it starts running, it may be compromised by installing malicious kernel modules later.

## Slide 3: Secure OS Monitoring is not Easy
Running on top of the OS
  Monitoring systems must issue system calls to the OS
    e.g. obtaining process information
    e.g. reading the kernel memory
  The results cannot be trusted if the OS is compromised
Embedded into the OS
  Monitoring systems can directly examine the kernel
  They are easily disabled by the compromised OS
OS
monitoring
system
monitoring
system
system calls
Notes: However, securely monitoring OSes is not easy.
Monitoring systems often run on top of the OS like applications.
For example, they can check whether malicious processes are running or not by obtaining process information via the proc filesystem.
They can check the integrity of the kernel by reading the kernel memory via the kmem device file.
To obtain such information, monitoring systems must issue system calls to the OS.
If the OS is compromised, the results cannot be trusted.
The compromised OS may hide malicious processes and return the correct kernel image.
On the other hand, monitoring systems can be embedded into the OS using kernel modules.
They can directly examine the kernel memory without relying on system calls or even kernel functions.
For example, they can directly traverse the process list.
However, they can easily disabled by the compromised OS.

## Slide 4: VM-based Approaches
Two approaches have been proposed
  The underlying hypervisor monitors the OS in a virtual machine (VM)
  A privileged VM monitors the OS in a target VM
The hypervisor and the privileged VM can be also compromised
  There are vulnerabilities in software
hypervisor
OS
monitoring
system
monitoring
system
privileged
VM
target
VM
Notes:   To solve this problem, many researchers have proposed methods for monitoring OSes with the virtual machine technology.
  There are two VM-based approaches.
  One is that the underlying hypervisor monitors the OS in a VM.
  The hypervisor can access the kernel memory of a VM directly.
  Since the hypervisor is isolated from VMs, monitoring systems can securely monitor OSes.
  Monitoring systems in the hypervisor don't rely on the OS and they aren't disabled by a compromised OS.
  The other approach is that a privileged VM monitors the OS in a target VM.
  The privileged VM can access the kernel memory of a target VM via hypervisor's functions.
  Since the privileged VM is also isolated from VMs, monitoring systems can perform secure OS monitoring.
  However, the hypervisor and the privileged VM can be also compromised from a target VM.
  Since they are constructed by software, there can be vulnerabilities used by attackers in the target VM.
  In fact, such vulnerabilities have been reported.

## Slide 5: Hardware-based Approaches
Using System Management Mode (SMM) in x86
  One of many hardware-based approaches
  A CPU can securely execute a monitoring system in SMM
    A monitoring system is located in isolated SMRAM
Several drawbacks
  SMM is much slower than the normal mode
  A monitoring system must be embedded in BIOS
monitoring
system
SMRAM
SMM
main
memory
normal
mode
CPU
Notes: To avoid software vulnerabilities, many hardware-based approaches have been proposed.
One of them is using System Management Mode (SMM) in x86 processors.
SMM is one mode of a CPU and, for example, used for power management.
A monitoring system is located in isolated memory called SMRAM.
SMRAM cannot be accessed in the normal mode of a CPU.
It can be accessed only in SMM.
When a CPU enters SMM by special interrupts, it can securely execute the monitoring system in SMRAM.
Attackers cannot modify the contents of SMRAM because a regular system including the OS runs in the normal mode.
However, there are several drawbacks in SMM.
First, SMM is much slower than the normal mode.
Second, a monitoring system must be embedded in BIOS to load it to SMRAM.
This makes the development of monitoring systems difficult.

## Slide 6: SPE Observer
A framework for securely monitoring OSes using Cell/B.E.
  Runs a monitoring system on an SPE
    An SPE is a general-purpose CPU core
    Its isolation mode enables secure execution
  Monitors the running status of the monitoring system from an external security proxy
PPE
OS
SPE
monitoring
system
security
proxy
target
host
Cell/B.E.
Notes: So, we propose SPE Observer, which is a framework for securely monitoring OSes using a Cell/B.E. processor.
SPE Observer runs a monitoring system on an SPE.
An SPE is one of the general-purpose CPU cores in Cell/B.E.
I'll explain the detailed architecture of Cell/B.E. in the next slide.
The isolation mode of an SPE enables secure execution of a monitoring system.
As a result, SPE Observer can preserve the integrity and confidentiality of the monitoring system.
In addition, SPE Observer monitors the running status of the monitoring system on the SPE from an external security proxy.
This guarantees the availability of the monitoring system while the system is running.
Later, I'll explain why the security proxy is necessary.

## Slide 7: Architecture of Cell/B.E.
Heterogeneous multicore processor
  PPE (control processing core)
    Runs the OS and regular processes
  SPE (arithmetic processing core)
    Runs parallel applications
    Contains the memory called a local store
    Accesses the main memory using DMA
SPE
SPE
SPE
SPE
SPE
SPE
PPE
main
memory
local
store
DMA
DMA
Notes: Cell/B.E. is a heterogeneous multicore processor.
As examples, it is used in PlayStation 3 and Toshiba's high-end TVs.
A PPE is a control processing core and runs the OS and regular processes.
The PPE can access the main memory directly.
On the other hand, an SPE is an arithmetic processing core and runs parallel applications.
Each SPE contains the memory called a local store, which is physically isolated from the PPE and the other SPEs.
The local store can be accessed from the other cores using DMA.
Also, an SPE accesses the main memory using DMA.

## Slide 8: Isolation Mode
Protects the local store in an SPE from the PPE and the other SPEs
  Preserving integrity
    Attackers cannot modify a running monitoring system or processing data
  Preserving confidentiality
    Attackers cannot analyze a monitoring system or steal sensitive information
isolated SPE
monitoring
system
local store
PPE
SPE
OS
application
Notes: As I explained, the PPE and SPEs can access the local stores in other SPEs.
This means that the compromised OS running on the PPE and malicious applications on SPEs can attack the monitoring system in another SPE.
The isolation mode of an SPE can protect the local store from the other CPU cores.
In other words, the other CPU cores cannot access the local store of isolated SPE.
Using the isolation mode, the integrity of a monitoring system is preserved.
Since the code and data are located in the protected local store, attackers cannot modify a running monitoring system or its processing data.
As a result, the monitoring system can run without interferences and detect a compromised OS correctly.
The confidentiality of the monitoring system is also preserved.
Attackers cannot analyze a running monitoring system or steal its sensitive information such as secret keys used by it.

## Slide 9: Secure Loader
Securely loads a monitoring system into the local store of an isolated SPE
  Preserving integrity
    Attackers cannot load compromised images of monitoring systems
  Preserving confidentiality
    Attackers cannot decrypt images of monitoring systems
main
memory
encrypted
image
encrypted
image
monitoring system
DMA
isolated SPE
DMA
secure loader
verify & decrypt
verify & decrypt
Notes: SPE Observer securely loads a monitoring system into the local store of an isolated SPE using a secure loader.
First, it loads an encrypted image of the secure loader into the local store of an isolated SPE.
The SPE verifies the digital signature of the image and decrypts the secure loader with the secret key embedded into the hardware.
Next, the secure loader loads an encrypted image of a monitoring system into the local store.
It verifies the digital signature of the image and decrypts the monitoring system with its secret key.
The secure loader preserves the integrity and confidentiality of the images of monitoring systems.
For the integrity, attackers cannot load compromised or malicious images of monitoring systems.
For the confidentiality, attackers cannot decrypt the encrypted images of monitoring systems.

## Slide 10: Availability Issue
The isolation mode is not perfect for secure execution of monitoring systems
  The PPE can stop the execution of even isolated SPEs
    It must control all the SPEs
Attackers can disable monitoring systems!
  The isolation mode is not designed for PPE monitoring
  Fortunately, the confidentiality of monitoring systems is still preserved
PPE
OS
isolated SPE
monitoring
system
stop
Notes: As such, the isolation mode can preserve the integrity and confidentiality, but it is not perfect for secure execution of monitoring systems.
The PPE can stop the execution of even isolated SPEs although it cannot access the protected local stores.
This is because the PPE must control all the SPEs in the normal use of Cell/B.E.
If an application on an SPE loops infinitely, the PPE needs to stop it.
However, this function is critical when an SPE monitors the PPE.
Attackers can disable monitoring systems.
The root cause of this is that the isolation mode of an SPE is not designed for monitoring the PPE.
Fortunately, the confidentiality of monitoring systems is still preserved when the PPE stops an isolated SPE.
Since the contents of its local store is automatically erased by hardware, even the PPE cannot steal sensitive information.

## Slide 11: Security Proxy
Externally monitors the running status of monitoring systems on SPEs
  Periodically sends heartbeats to monitoring systems via the relay process
Cuts the network if monitoring systems do not respond to the heartbeats correctly
PPE
SPE
monitoring
system
security
proxy
external
network
heartbeats
relay
process
target host
OS
internal
network
Notes: To solve this availability issue, SPE Observer uses an external security proxy.
The security proxy monitors the running status of monitoring systems on isolated SPEs.
It is a network bridge between the target host and the external network.
It periodically sends heartbeats to a monitoring system and checks its liveness.
The heartbeats are sent via the relay process on the PPE.
The relay process is necessary because it must communicate with the security proxy using the TCP/IP stack implemented in the OS.
It is difficult that a monitoring system itself directly communicates with the security proxy because the local store of an SPE is too small to implement its own TCP/IP stack.
If a monitoring system does not respond to heartbeats correctly, such as no response or invalid responses, the security proxy detects that the monitoring system does not run correctly.
In this case, the security proxy cuts the internal network and isolates the target host from the network.

## Slide 12: Secure Heartbeats
The security proxy sends an encrypted challenge to a monitoring system
  The monitoring system decrypts it and returns an encrypted response
Attackers cannot return correct responses
  Only legitimate monitoring systems and the security proxy share secret keys
    A malicious relay process cannot mount man-in-the-middle attacks
security
proxy
monitoring
system
relay
process
encrypted
challenge
encrypted
response
Notes: For secure heartbeats, the security proxy sends an encrypted message for a challenge to a monitoring system via the relay process.
When the monitoring system receives the challenge, it decrypts the message and returns an encrypted response based on the challenge to the security proxy via the relay process.
Attackers cannot return correct responses to the security proxy because only a legitimate monitoring system can do.
The secret key necessary for encryption and decryption is shared between the security proxy and the monitoring system.
Attackers cannot steal the secret key in the local store of an isolated SPE.
In addition, even if attackers replace a relay process with malicious one, the malicious relay process cannot mount man-in-the-middle attacks because the secret key is pre-shared.

## Slide 13: Scheduled Monitoring
SPE Observer can schedule monitoring systems
  Application performance is improved by not occupying one SPE for a monitoring system
  Scheduling by the security proxy and the SPE scheduler
    The security proxy periodically sends commands
    The OS schedules SPEs if necessary
PPE
OS
SPE
security
proxy
commands
relay
process
SPE
SPE
application
...
...
monitoring
system
Notes: Cell/B.E. is a processor that gains performance by parallel processing with many SPEs, but SPE Observer needs at least one SPE for a monitoring system.
To mitigate the performance degradation, SPE Observer can schedule monitoring systems.
While a monitoring system is not running, it can release an SPE and applications can use it.
By not always occupying one SPE for a monitoring system, application performance is improved.
The scheduling of monitoring systems is performed by the security proxy and the SPE scheduler in the OS.
The security proxy periodically sends commands to the relay process.
The relay process loads a monitoring system to one of the SPEs.
If there is no idle SPE, the OS suspends one application thread on an SPE and runs a monitoring system on the SPE.
When a monitoring system terminates, the OS resumes the suspended thread.
Even if the relay process or the OS is compromised and does not start a monitoring system correctly, the security proxy can detect that using heartbeats.

## Slide 14: Examples of Monitoring Systems
Integrity monitor for the OS kernel
  Obtains the contents of the kernel memory using DMA
  Calculates SHA-1 hash and compares it with correct one
  Overlaps DMA with calculation using double buffering
Other possible monitors
  Monitors for dynamic kernel data
    Using a technique similar to VM introspection
PPE
OS kernel
SPE
integrity
monitor
DMA
SHA-1
DMA
buffers
DMA
SHA-1
Notes: As an example, we have developed an integrity monitor for the OS kernel.
This monitor obtains the contents of the kernel memory using DMA transfers from the main memory.
The obtained contents include kernel code and its read-only data.
Then the monitor calculates SHA-1 hash and compares it with correct one.
If the two values are different, the monitor can detect the modification to the OS.
To hide the overhead of DMA transfers, the integrity monitor overlaps DMA transfers with hash calculation using double buffering.
While the monitor calculates the hash value of the memory block in one buffer, the next memory block is transferred to the other buffer in parallel using DMA.
This is repeated with buffers swapped.
This is a very simple monitoring system, but there are other possible monitors.
For example, monitors for dynamic kernel data can check kernel data structures like process data.
This can be done by using a technique similar to virtual machine introspection, which is used for monitoring the OS from the outside of a virtual machine.

## Slide 15: Accessing the Kernel Memory
SPE Observer configures an isolated SPE to enable accessing the kernel memory
  Clears the Problem-State bit in the status register of the MFC
    The MFC is used for DMA transfers
  Registers an address mapping for the kernel memory to the SLB
    The SLB is an address translation table
local store
MFC
SLB
kernel memory
main
memory
SPE
DMA
Notes: In any monitoring systems, an SPE must access the kernel memory.
However, an SPE can access only the process memory by default.
So, SPE Observer configures an isolated SPE to enable accessing the kernel memory.
First, it clears the Problem-State bit in the status register of the MFC in an SPE.
The MFC is used to perform DMA transfers.
If this bit is cleared, the MFC can transfer the contents of the kernel memory.
Second, SPE Observer registers an address mapping for the kernel memory to the SLB of an SPE.
The SLB is an address translation table used by the MFC.
If there is an entry for the kernel memory in the SLB, the MFC can resolve the kernel address.

## Slide 16: Experiments
We conducted several experiments to examine
  Effectiveness and performance of the integrity monitor
  Impacts on application performance
We used the emulation of the isolation mode
  because we could not obtain the secure loader supporting the hardware-level isolation mode
CPU: 1 PPE, 6 SPEs
Local store: 256 KB
Main memory: 256 MB
NIC: Gigabit Ethernet
OS: Linux 2.6.27
CPU: Xeon E5630
Memory: 4 GB
NIC: Gigabit Ethernet
PlayStation 3
Security proxy
Notes: We conducted several experiments.
One aim is to examine the effectiveness and performance of the integrity monitor.
The other aim is to examine the impacts on application performance.
In these experiments, we used PlayStation 3, which had one PPE and six SPEs.
Each SPE had a local store of 256 KB.
We used the emulation of the isolation mode because we could not obtain the secure loader supporting the hardware-level isolation mode.

## Slide 17: Integrity Check of the Kernel
We ran the integrity monitor on an SPE
  It could detect the compromised kernels
    Modified system call table
    Modified function for a system call
We measured the time for integrity check
  Hash calculation: 70%
  DMA was hidden by calculation
Chart: time (ms)
| 項目 1
hash calculation | 17
heartbeat | 7
Notes: First, we ran the integrity monitor on an SPE.
In this experiment, we used the original kernel and two compromised kernels.
For one kernel, we modified the system call table.
For another kernel, we modified functions for a system call.
As a result, the integrity monitor could detect the compromised kernels correctly.
Then, we measured the time needed for the integrity check.
The integrity monitor obtained 12 MB of the kernel memory by DMA.
It took 24 ms in total.
70% was for hash calculation and the most of the rest was for responses to heartbeats.
DMA transfers were hidden by calculation.

## Slide 18: Impacts on Application Performance
We ran various applications with various monitors
  CPU- and DMA-bound applications
    Using various numbers of SPEs
  CPU- and DMA-bound monitors
    Using one SPE
main
memory
SPE
SPE
monitoring
system
SPE
SPE
SPE
SPE
CPU-bound
application
DMA
DMA-bound
monitor
Notes: To examine the impacts on application performance, we ran various applications with various monitors.
For applications, we used CPU-bound and DMA-bound applications.
For monitoring systems, we used CPU-bound and DMA-bound monitors.
We ran one monitor on one SPE and ran applications on several SPEs.
Then we measured the performance improvement when the number of SPEs increased.

## Slide 19: Impacts on Application Performance
We ran various applications with various monitors
  Any monitors did not affect CPU-bound applications
    Linear performance improvement
  All monitors affected DMA-bound applications
    Especially DMA-bound monitors
Chart: CPU-bound Application
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0
CPU-bound monitor | 1 | 2 | 3 | 4 | 5
Chart: DMA-bound Application
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0
CPU-bound monitor | 1 | 1.76 | 2.12 | 2.19 | 2.2
DMA-bound monitor | 0.88 | 1.41 | 1.64 | 1.76 | 1.84
Notes: Left figure is the results of a CPU-bound application.
The x-axis is the number of SPEs and the y-axis is the performance improvement.
CPU-bound and DMA-bound monitors were the same result.
The performance improvement was linear.
If the number of SPEs became 5, the performance improvement was 5 times.
This means that any monitors did not affect CPU-bound applications.
Right figure is the results of a DMA-bound application.
All monitors affected the DMA-bound application.
Even if the number of SPEs became 5, the performance improvement was only about 2 times.
Especially, a DMA-bound monitor conflicted with the DMA-bound application.

## Slide 20: Performance Degradation
We ran various applications using 6 threads with the integrity monitor
  The monitor occupied one SPE
    An application could use only 5 SPEs
SPE
integrity
monitor
SPE
thread
1
application
SPE
thread
2
SPE
thread
3
SPE
thread
4
SPE
thread
5
thread
6
Notes: To examine the performance degradation due to SPE Observer, we ran various applications using 6 threads with one integrity monitor.
The monitor always occupied one SPE and so the application could use only 5 SPEs.
6 application threads used 5 SPEs with context switches.
For comparison, we measured the performance when we did not run the monitor and the application used 6 SPEs.

## Slide 21: Performance Degradation
We ran various applications using 6 threads with the integrity monitor
  The monitor occupied one SPE
    An application could use only 5 SPEs
Application performance
  CPU-bound: 83% (= 5/6)
  DMA-bound: 98%
    DMA bandwidth was saturated
  Matrix: 18%
    Waiting for synchronization
Chart: performance
| 項目 1
CPU-bound | 0.83
DMA-bound | 0.98
Matrix | 0.18
Notes: Here is the result of three applications.
The y-axis is the relative performance.
For a CPU-bound application, the performance became 83% by using one SPE for the monitor.
This is five-sixth and an expected result.
For a DMA-bound application, the performance degraded only by 2%.
This is because DMA bandwidth was almost saturated even in 5 SPEs and the performance was not improved in 6 SPEs.
On the other hand, for matrix multiplication, the performance degraded extraordinarily to 18%.
This application synchronized between all the threads after each thread performed a small amount of computation.
Since one thread is delayed for waiting for an SPE, the others must wait for the thread.

## Slide 22: Improvement by Scheduling (1/2)
SPE Observer scheduled the integrity monitor at various intervals
  We measured the performance of matrix multiplication
SPE
integrity
monitor
SPE
thread
1
application
SPE
thread
2
SPE
thread
3
SPE
thread
4
SPE
thread
5
thread
6
Notes: To examine the improvement by scheduling monitoring systems, we measured the application performance when SPE Observer scheduled the integrity monitor at various intervals.
In scheduled monitoring, while the monitor was not running, the application could use 6 SPEs.
When the monitor started running again, one thread is suspended.

## Slide 23: Improvement by Scheduling (1/2)
SPE Observer scheduled the integrity monitor at various intervals
  We measured the performance of matrix multiplication
The performance was improved
  as the interval became longer
  83% at a 200-ms interval
    = 5/6
Chart: Matrix
| 0.0 | 100.0 | 200.0 | 300.0 | 400.0 | 500.0 | 600.0 | 700.0 | 800.0 | 900.0 | 1000.0
scheduling | 0.442 | 0.771 | 0.835 | 0.905 | 0.925 | 0.943 | 0.953 | 0.956 | 0.955 | 0.967 | 0.98
no scheduling | 0.18 | 0.18 | 0.18 | 0.18 | 0.18 | 0.18 | 0.18 | 0.18 | 0.18 | 0.18 | 0.18
Notes: Here is the result of matrix multiplication.
The x-axis is the scheduling interval and the y-axis is the relative performance.
The red line is the performance when scheduling was not performed.
The blue line is that when scheduling was performed at some interval.
The performance was improved as the interval became longer.
It exceeded 83% at a 200-ms interval.

## Slide 24: Improvement by Scheduling (2/2)
We measured the performance of CPU- and DMA-bound applications
  CPU-bound: 96% at a 100-ms interval
  DMA-bound: almost 100% at a short interval
Chart: CPU-bound Application
| 0.0 | 100.0 | 200.0 | 300.0 | 400.0 | 500.0 | 600.0 | 700.0 | 800.0 | 900.0 | 1000.0
scheduling | 0.84 | 0.96 | 0.98 | 0.985 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99 | 0.99
no scheduling | 0.83 | 0.83 | 0.83 | 0.83 | 0.83 | 0.83 | 0.83 | 0.83 | 0.83 | 0.83 | 0.83
Chart: DMA-bound Application
| 0.0 | 100.0 | 200.0 | 300.0 | 400.0 | 500.0 | 600.0 | 700.0 | 800.0 | 900.0 | 1000.0
scheduling | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
no scheduling | 0.98 | 0.98 | 0.98 | 0.98 | 0.98 | 0.98 | 0.98 | 0.98 | 0.98 | 0.98 | 0.98
Notes: To examine the impacts on scheduling for other applications, we measured the performance of CPU- and DMA-bound applications.
Left figure is the performance of a CPU-bound application.
The performance was 83% when no scheduling was performed.
The performance was improved by scheduled monitoring and 96% at a 100-ms interval.
Right figure is the performance of a DMA-bound application.
The performance was 98% even under no scheduling, but it became almost 100% at a short interval.

## Slide 25: Related Work
Copilot [Petroni et al.'04]
  Sends the contents of the physical memory to a remote host using a special PCI card
    The remote host checks the integrity of the OS
Flicker [McCune et al.'08]
  Executes security-sensitive code using Intel TXT
  The whole system is suspended while such code is running
Code verification service [Murase et al.'09]
  An isolated SPE checks the integrity of applications for running on the PPE
  Not assume that the OS is compromised
Notes: Copilot sends the contents of the physical memory to a remote host using a special PCI card.
Then the remote host checks the integrity of the OS.
Copilot needs special hardware, but SPE Observer uses only general-purpose hardware although Cell/B.E. is a bit special.
Flicker securely executes security-sensitive code using Intel TXT or AMD SVM.
While such code is running, the whole system including the OS is suspended.
In SPE Observer, the OS and applications can run with monitoring systems.
Code verification service using the isolation mode has been proposed.
An isolated SPE checks the integrity of applications for running on the PPE.
This system does not assume that the OS is compromised.

## Slide 26: Conclusion
We proposed SPE Observer
  A framework for secure execution of OS monitoring systems
  Using the isolation mode of SPEs
    to guarantee the integrity and confidentiality
  Using the security proxy
    to monitor the running status of monitoring systems
  Scheduling monitoring systems
    to mitigate performance degradation
Future work
  Developing various monitoring systems
  Developing middleware for better SPE scheduling
Notes: In conclusion, we proposed SPE Observer, which is a framework for secure execution of OS monitoring systems.
SPE Observer uses the isolation mode of SPEs to guarantee the integrity and confidentiality of monitoring systems.
It also uses the security proxy to monitor the running status of monitoring systems.
The security proxy complements the imperfection of the isolation mode.
In addition, SPE Observer can schedule monitoring systems to mitigate performance degradation of parallel applications.
One of our future work is developing various monitoring systems.
Currently, we have developed only the integrity monitor for the OS kernel.
We are planning to implement monitoring systems with VM-introspection-like techniques.
Another direction is developing middleware for better SPE scheduling.
In the current implementation, the OS cannot detect idle SPEs waiting for synchronization.
We need middleware running in SPEs to notify idleness to the OS.