## Slide 1: Keyspector: Secure Monitoring of IoT Devices Using RISC-V Keystone
Takahito Iwano and Kenichi Kourai
Kyushu Institute of Technology, Japan
Notes: I’m Takahito Iwano from Kyushu Institute of Technology.
I’m gonna talk about Keyspector: Secure Monitoring of IoT Devices Using RISC-V Keystone.

## Slide 2: Attacks against IoT Devices
Internet of Things (IoT) has rapidly proliferated in recent years
  IoT devices are expected to increase to 40.6 billion by 2034
  Examples of IoT devices: home routers, printers, TVs, and cars
IoT devices are exposed to a high risk of attacks
  Detected IoT malware increased by 45% between 2023 and 2024
  E.g., Denial-of-service attacks, unauthorized modification of programs
Internet
attacker
Notes: The Internet of Things (IoT) has rapidly proliferated in recent years.
The number of IoT devices is expected to increase to 40.6 billion by 2034.
Since IoT devices, such as home routers, printers, TVs, and cars, are connected to servers or other devices via the Internet.
IoT devices are exposed to a high risk of attacks.
In fact, between 2023 and 2024, the number of detected malware targeting IoT devices increased by 45% year over year.
Examples of such attacks include distributed denial-of-service attacks by exploiting compromised IoT devices.
Incidents involving unauthorized modification of programs running inside IoT devices also occur.

## Slide 3: Secure Execution of IDS
Intrusion detection systems (IDS) are used to detect attacks
  Not easy to securely execute host-based IDS
  IDS itself may be tampered with by intruders
Securely executed with trusted execution environments (TEEs)
  Security feature provided by recent processors
  Protect IDS even from the operating system
intruder
OS
IDS
target system
IDS
IDS
TEE
Notes: IDS monitors abnormal behaviors of the system inside an IoT device and notifies administrators of possible intrusions.
However, it is not easy to securely execute host-based IDS inside a target system.
Once the system is compromised, IDS itself may be tampered with by intruders. Although IDS can be protected by running it inside the OS, even such IDS can be compromised if the OS contains vulnerabilities.
To securely execute IDS, using trusted execution environments (TEEs) provided by recent processors has been proposed.
Using a TEE allows programs to run securely in logically isolated memory regions.
If you use a TEE, it can protect the IDS even from the operating system.

## Slide 4: Protecting IDS with Intel SGX
BIOS
Execute IDS in a protection domain called an SGX enclave
  Verify the digital signature of the code running in an enclave
  Encrypt and integrity-check enclave memory
Monitor OS data in system memory [Koga+, TrustCom’23]
  An enclave in an application cannot directly access system memory
  Obtain memory data via BIOS in System Management Mode (SMM)
target
system
OS
enclave
IDS
monitor
Notes: For example, a method that securely executes IDS using Intel SGX has been proposed.
IDS can be securely executed inside a protection domain called an SGX enclave on top of the OS.
SGX ensures the integrity of the enclave memory and thereby prevents attackers from modifying the running code.
Since the enclave memory is encrypted, data inside the enclave cannot be eavesdropped on by attackers.
IDS in an enclave monitors system information by accessing the memory of the target system.
However, it cannot directly access the system memory because an SGX enclave has the same privileges as an application.
Therefore, it invokes BIOS running below the OS and securely obtains the memory data of the OS using System Management Mode (SMM).

## Slide 5: Issues of Using SGX
Significant overhead in memory data acquisition
  IDS must invoke BIOS using System Management Interrupts
  Memory data must be encrypted and integrity-checked
  The entire system is halted while the SMM program is executed
Cannot be applied to IoT devices
  SGX is currently supported only on server-grade processors
BIOS
target
system
OS
enclave
IDS
SMM program
SMI
access
halt
Notes: However, this system incur significant overhead in obtaining memory data.
IDS in an enclave must invoke BIOS by generating system management interrupts.
To prevent eavesdropping and tampering by the untrusted application code or an untrusted OS,
the enclave and the SMM program in BIOS need to encrypt and integrity-check exchanged data.
In addition, the entire target system is halted while the SMM program is executed in BIOS.
Furthermore, SGX is currently supported only on server-grade Intel processors.
Previously, it was possible to use SGX on desktop PCs
Thus, it cannot be applied to IoT devices.

## Slide 6: Protecting IDS with Arm TrustZone
monitor
Execute IDS in the secure world of TrustZone [Guerra+, QRS’18]
  Monitor OS data in the normal world
  Directly access the system memory of the normal world
  Arm processors are commonly used in IoT devices
The secure world has higher privileges than necessary
  Developing IDS in the secure world requires great caution
secure monitor
IDS
trusted OS
OS
application
normal world (target system)
secure world
TA
TA
Notes: On the other hand, Arm processors provide a TEE called TrustZone.
They are commonly used in IoT devices.
TrustZone provides two execution environments known as worlds.
A method that executes IDS in the secure world of TrustZone has also been proposed.
In this approach, the IDS monitors OS data in the normal world and directly accesses its system memory.
However, the secure world has higher privileges than necessary for IDS.
In fact, various vulnerabilities in TAs and the trusted OS have been reported.
If IDS is compromised, these high privileges may be taken over by attackers.
Therefore, developing IDS in the secure world requires great caution.
In fact, many devices do not allow users to execute custom TAs.

## Slide 7: Our Approach: Keyspector
Enable the secure execution of IDS using RISC-V Keystone
  Keystone is a TEE for RISC-V processors
  RISC-V is expected to be widely adopted in IoT devices
Execute IDS inside a Keystone enclave
  An enclave is strictly isolated from the target system
  The security monitor in the highest privilege enforces the isolation
security monitor
IDS
runtime
OS
application
target system
enclave
monitor
M-mode
Notes: As a new approach, we propose Keyspector for enabling the secure execution of IDS using RISC-V Keystone.
Keystone is a TEE for RISC-V processors.
RISC-V is an open-source instruction set architecture that has recently gained attention and is expected to be widely adopted in IoT devices.
Keyspector executes IDS inside a Keystone enclave and prevents it from being eavesdropped on or tampered with.
Both the enclave and the target system run on top of the security monitor and are strictly isolated from each other.
The security monitor is software running in the highest privilege called M-mode.

## Slide 8: Advantages of Keyspector
Allow IDS to directly access system memory unlike SGX
  Not rely on trusted components (BIOS) to obtain memory data
  Not need to encrypt or integrity-check obtained memory data
Can protect the target system from erroneous IDS
  An enclave has lower privileges than the secure world in TrustZone
  IDS cannot destroy system memory
target system
enclave
IDS
OS
application
read
system memory
write
Notes: Keyspector allows its enclave to directly access the entire system memory unlike SGX.
To access the system memory, an SGX enclave must rely on external trusted components such as BIOS and perform indirect memory access.
Therefore, data protection mechanisms are required between the enclave and the external component.
In contrast, Keyspector eliminates the overhead of the indirect memory access and the encryption and integrity checks.
In Keyspector, no excessive privileges are granted, so it can protect the target system from an erroneous IDS.
Since an enclave has lower privileges than the secure world in TrustZone, the IDS cannot destroy the system memory.

## Slide 9: Monitoring the State of Enclaves
Intruders can stop the low-privileged enclave running IDS
  The target system can create, run, and terminate enclaves
  Difficult to prevent this type of attack
The security monitor inspects the state of the enclave
  Check for the presence of the enclave
  Confirm that the enclave is periodically scheduled
security monitor
IDS
runtime
target system
enclave
process
create
monitor
intruder
Notes: Since enclaves are low-privileged, intruders inside the target system can stop the enclave running IDS easily.
In Keyspector, the target system creates, runs, and terminates enclaves.
Therefore, if intruders gain administrative privileges in the target system, they could forcibly terminate the enclave and disable the IDS.
Since it is difficult to prevent this type of attack, the security monitor periodically checks for the presence of the enclave running IDS and detects the unauthorized termination of IDS.
Even if intruders do not terminate the enclave, they could prevent the enclave from being scheduled.
Therefore, the security monitor confirms that the enclave is periodically scheduled by monitoring context switches.

## Slide 10: Threat Model
Trust RISC-V processors and the security monitor
  Attackers cannot intrude into enclaves running IDS
Attackers intrude into the target system via networks
  Take root privileges and control the OS and enclaves completely
  Create new enclaves and terminate existing enclaves
  Change the scheduling of enclaves
target system
security monitor
IDS in an enclave
IDS
runtime
OS
application
RISC-V processors
untrusted
trusted
Notes: The threat model of Keyspector is as follows.
We assume that RISC-V processors and the security monitor are trusted and free of vulnerabilities.
Also, we assume that attackers cannot intrude into enclaves running IDS by exploiting the vulnerabilities of software inside the enclaves.
As for attacks on the target system, we assume attackers who attempt to compromise the system remotely over the network.
Attackers inside the target system can take root privileges and control the OS and enclaves completely.
They can create new enclaves and terminate existing enclaves, including ones running IDS.
In addition, they can change the scheduling of enclaves.

## Slide 11: Basics of Memory Access Control
Use Physical Memory Protection (PMP) in RISC-V processors
  PMP restricts software access to physical memory regions
The security monitor re-configures PMP on context switches
  Enable access to enclave memory when switching to the enclave
  Disable access to the memory of the target system
    The enclave cannot access system memory to obtain OS data
system
enclave
system
enclave
system running
enclave running
full access
no access
physical
memory
target
system
enclave
IDS
target
system
enclave
IDS
Notes: In RISC-V processors, memory access control can be done using physical memory protection (PMP).
PMP restricts software access to physical memory regions.
In Keystone, the security monitor re-configures PMP on context switches.
When switching the context from the target system to an enclave, the security monitor disables access to the system memory and enables
access only to the physical memory assigned to the enclave.
Conversely, when switching the context from the enclave back to the host system, the security monitor enables access to the system memory and disables access to the memory assigned to the enclave.
Therefore, the enclave cannot access the system memory to obtain OS data.

## Slide 12: Sharing System Memory with Enclaves
Upon switching to the enclave
  Enable only read only access to system memory for the enclave
  Not permit write access to system memory
    The enclave does not affect the target system erroneously
Upon switching to the target system
  Enable full access to system memory
full access
read-only access
no access
system
enclave
system
enclave
system running
enclave running
physical
memory
target
system
enclave
IDS
target
system
enclave
IDS
Notes: In Keyspector, we changed this reconfiguration in the security monitor.
When switching the context from the target system to the enclave running IDS, the security monitor enables read access to the system memory, instead of completely disabling access.
This allows the enclave to directly monitor the system memory.
Since the security monitor does not allow the enclave to modify the system memory, the enclave does not affect the behavior of the host system erroneously.
When switching the context from the enclave to the host system, the security monitor enables all access to the system memory so that the host system can access its memory without any restrictions.

## Slide 13: Controlled Sharing with the Security Monitor
It is not secure for all enclaves to access system memory
  Attackers can create enclaves and eavesdrop on OS data
Limit enclaves that can share system memory
  Calculate the hash value of software running inside an enclave
  The security monitor compares it with that of pre-registered IDS
  Permit memory sharing to that enclave only if the hash value matches
security monitor
IDS
runtime
loader
96eff78726d3a251cc49decb4048cd
hash value
calculate
96eff78726d3a251cc49decb4048cd
pre-registered hash value
compare
enclave
Notes: If all the enclaves were permitted to share the system memory, the intruders who compromise the target system could execute malicious enclaves to eavesdrop on OS data in the system memory.
To address this issue, the security monitor allows access to the system memory only for the enclave in which IDS is running.
It calculates the hash value of the software running inside the enclave.
Originally, this hash value is used for remote attestation to confirm that the software is not tampered with at boot time.
In Keyspector, the security monitor additionally checks that the hash value matches that of a pre-registered IDS and grants access to the system memory only for the enclave running the pre-registered IDS.

## Slide 14: Controlled Sharing with Remote Attestation
Can integrate controlled sharing with remote attestation
  The security monitor generates a signed report for the hash value
    Send the report to the attestation server via the target system
  The attestation server checks the received hash value
Easier to update IDS running in enclaves
  Can register hash values without modifying the security monitor
target system
security monitor
enclave
report
IoT device
IDS
attestation server
generate
message
check
generate
Notes: As an alternative approach, this controlled memory sharing can be integrated with remote attestation.
First, the security monitor calculates the hash value of software running inside an enclave
and generates a signed report including the hash value. Then, it
sends the signed report to the attestation
server via the target system. The attestation server checks whether the
received hash value matches that for the pre-registered IDS. Then, it
sends the matching result back to the security monitor. The security monitor
verifies the received message.
One advantage of this method is that the hash value of a new IDS can be registered without modifying the security monitor.

## Slide 15: Accessing System Memory
Enable IDS to directly access system memory in an enclave
  IDS is a process running on top of a lightweight OS called runtime
  Both IDS and the runtime are loaded by the loader at boot time
  The loader directly maps system memory onto IDS
IDS must access system memory in physical addresses
  Add the address of the mapped system memory as an offset
physical memory
IDS
runtime
map
map
enclave
system
enclave
target system
Notes: Keyspector allows IDS in an enclave to directly access the system memory.
In Keyspector, IDS is created as a process and runs on top of a lightweight OS called runtime.
When an enclave is launched, the loader is first executed and then loads
the runtime and IDS in the enclave. At this stage, the loader maps the
physical memory assigned to the enclave onto the kernel address space
of the runtime. In Keyspector, the loader additionally maps the
system memory onto the process address space.
IDS must access the mapped system memory in physical addresses.
It adds the address of the mapped system memory to the target physical address as an offset.

## Slide 16: Accessing OS Data
IDS obtains OS data from the mapped system memory
  Translate the virtual address of OS data into a physical address
  Need the page tables used in the target system
Obtain the address of the page table from the satp register
  The register value is saved in the security monitor on a context switch
  IDS invokes the security monitor via the runtime
enclave
IDS
runtime
security monitor
satp register value
SBI call
system call
target system
page
table
Notes: IDS in an enclave obtains the OS data of the target system from the system memory.
To access OS data, it needs to translate the virtual address of the OS data into a physical address.
This address translation can be done using the page tables of the target system, which are stored in the system memory.
The physical address of the page tables is held in the satp register in RISC-V.
The value of the satp register used by the target system is saved in the security monitor when the context is switched from the target system.
Therefore, IDS first invokes the runtime, and then the runtime invokes the security monitor.

## Slide 17: Address Translation for RISC-V
IDS walks the page tables to find a physical address
  Obtain the address translation mode from the satp register
  The current implementation supports Sv39 and Sv57
    E.g., Sv39 uses 39-bit virtual addresses and three-level page tables
Cache the results of the address translation
  Not walk the page tables for virtual addresses in the same page
target system
page table
enclave
IDS
runtime
cache
Notes: Using the obtained physical address of the page tables, IDS walks
through the page tables to find the target physical address
corresponding to a given virtual address. Since RISC-V supports
multiple address translation modes, IDS obtains the used mode from the
satp register value. The
current implementation supports Sv39 and Sv57. For example, Sv39 uses 39-bit
virtual addresses and three-level page tables.
The result of the address translation is cached so that the page tables
are not walked again for virtual addresses that belong to the same
page.

## Slide 18: Developed IDS
Develop IDS using the LLView framework [Ozaki+, CLOUD’23]
  Write programs for analyzing OS data using the OS source code
  Embed the address translation of OS data into the programs
Our IDS collects information provided by the proc filesystem
  The proc filesystem is used by the OS in the target system
  E.g., information on processes, network sockets, and system resources
for_each_online_cpu(i) {
struct kernel_cpustat kcpustat;
kcpustat_cpu_fetch(&kcpustat, i);
idle = get_idle_time(&kcpustat, i);
:
}
IDS
LLView
OS source code
Notes: We have developed IDS using the LLView framework. LLView is a framework
that allows developers to write programs for analyzing OS data using
the OS source code. LLView embed the address translation of OS data into the programs at compile time.
Our IDS collects system information provided by the proc
filesystem in Linux. The proc filesystem generates pseudo files that
reflect the state of the Linux kernel and provides information about
processes, network sockets, and system
resources.

## Slide 19: Experiments
We conducted several experiments using the developed IDS
  Examine whether our IDS can detect IoT malware in an enclave
  Examine the IDS performance and the impact on the target system
Comparison
  Traditional IDS: Read the proc filesystem inside the target system
  An emulator and a real IoT device
 | emulator host
CPU | Core i7-14700
memory | 64GB
emulator | QEMU 6.2.0
 | emulator | real device
CPU | 4 cores | Freedom U740 SoC (4 cores)
memory | 2GB | 16GB
firmware | OpenSBI 1.1 | 
OS | Linux 6.1.32 | Linux 6.1.43
Notes: We conducted several experiments to examine the effectiveness of Keyspector.
First, we examined whether our IDS can detect IoT malware in an enclave.
Then, we examined the IDS performance and the impact on the target system.
For comparison, we used the traditional IDS that reads the
proc filesystem inside the target system. In this experiment, we used
both a RISC-V emulator and a real IoT device. For the emulator, we ran QEMU on a PC.

## Slide 20: Capability Tests of IDS
We executed our IDS inside an enclave using Keyspector
  IDS could correctly collect system information
  An illegitimate IDS could not eavesdrop on system memory
We examined whether our IDS could detect IoT malware
  IDS detected unauthorized communication and processes
unauthorized communication
unauthorized process
execution results of an illegitimate IDS
Notes: We executed our IDS inside an enclave using Keyspector.
As a result, the output of our IDS matched the information
obtained in the target system.
Next, we slightly modified the IDS program.
As you can see in the figure on the left, such an illegitimate IDS could not eavesdrop on the system memory.
Next, we examined whether our IDS could detect IoT
malware. First, we ran a program that performed communication to TCP
port number 2323, which was used by Mirai.
As you can see in the top right figure, our IDS could detect unauthorized communication from the list of TCP connections.
Second, we ran a program whose process name was dvrhelper, which was used by Mukashi, a variant of Mirai.
As you can see in the bottom right figure, our IDS could detect the unauthorized process from the process list.

## Slide 21: Collection Time of System Information
We measured the total time to collect system information
  7 types of global information and 3 types of process information
  50% shorter than the traditional IDS on the emulator
  10% longer on the real device
Chart: collection time (ms)
| emulator | real device
traditional IDS | 0.028948 | 0.021134
Keyspector | 0.014327 | 0.023271
 | emulator | real device
processes | 62 | 110
TCP connections | 1 | 4
tty drivers | 11 | 13
50% shorter
10% longer
Notes: To examine the IDS performance, we measured the total time required for the IDS to collect system
information provided by the proc file system using Keyspector and the
traditional IDS. These IDS collect 7 types of global information and 3 types of process information.
The table on the left shows the number of monitored objects in the target system.
Compared with the traditional method, Keyspector reduced the collection time by a factor of 2 on the emulator. In contrast, the collection time was 10% longer than the traditional IDS on the real device.

## Slide 22: Breakdown of the Collection Time
We examined the collection time for each system information
  Shorter or longer than the traditional IDS on the real device
  Shorter for almost all information on the emulator
The traditional IDS was much slower only on the emulator
  File access was slow on the emulator
Chart: 
| tcp | pid-auxv | pid-stat
traditional IDS | 0.0023199 | 0.0095955 | 0.012559
Keyspector | 0.0023191 | 0.00031168 | 0.0035611
emulator
real device
breakdown of the file collection time
(emulator)
Chart: collection time (ms)
| tcp | pid-auxv | pid-stat
traditional IDS | 0.0023199 | 0.0095955 | 0.0051445
Keyspector | 0.011506 | 8.65e-05 | 0.0043675
Chart: 
| file access | data generation
 | 0.044592 | 0.0060005
Notes: To investigate the large difference between the emulator and the real
device, we measured the time required to collect the system
information necessary for generating each pseudo file.
The two graphs on the left shows a part of the breakdown of the collection time.
On the real device, the collection time in Keyspector was shorter or longer than the traditional IDS. In contrast, it was shorter for
almost all pseudo files on the emulator.
We examined why the collection time was much longer in the traditional IDS only on the emulator.
The right-hand side figure shows the breakdown of the file collection time on the emulator.
From this result, we found that the cause was slower file access on the emulator.

## Slide 23: Collection Time of TCP information
Keyspector was slow in collecting TCP data on the real device
  The TCP hash table was 8x larger on the real device
  The number of address translations increased by 8x
  The collection time was proportional to # of address translations
Chart: 
| emulator | real device
 | 17488 | 139675
number of translations (tcp)
Chart: 
| emulator | real device
 | 17406 | 139262
total size of the TCP hash tables
8x
8x
Notes: For TCP information, the collection time was not so long on the emulator, but it was 5 times longer than the traditional IDS on the real device.
As a result of our inspection, we found that the total size of the hash tables
used to manage TCP connections in the kernel was 8 times larger on the real
device.
Since our IDS traversed the hash tables to obtain the list of
TCP connections, the number of address translations increased by a
factor of 8.
The collection time was proportional to the
number of address translations.
From this result, it was revealed that the overhead of
Keyspector came from address translation performed in software.

## Slide 24: Impact on System Performance
We executed sysbench in the target system
  IDS collected system information at 0-20s intervals
  The trend is similar on the emulator and the real device
  Performance degradation was 0.7-22%
real device
Chart: monitoring interval (sec)
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
with IDS | 2645.923 | 3044.343 | 3140.209 | 3252.597 | 3266.324 | 3290.502 | 3314.905 | 3321.577 | 3374.969 | 3360.661 | 3317.147
without IDS | 3397.327 | 3397.327 | 3397.327 | 3397.327 | 3397.327 | 3397.327 | 3397.327 | 3397.327 | 3397.327 | 3397.327 | 3397.327
emulator
Chart: monitoring interval (sec)
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
with IDS | 1230.742 | 1343.913 | 1400.32 | 1431.305 | 1451.208 | 1464.6 | 1481.766 | 1484.337 | 1498.996 | 1497.932 | 1507.632
without IDS | 1564.701 | 1564.701 | 1564.701 | 1564.701 | 1564.701 | 1564.701 | 1564.701 | 1564.701 | 1564.701 | 1564.701 | 1564.701
Notes: To examine the impact of the execution of IDS on system performance,
we executed the sysbench benchmark in the target system. Then, we measured the CPU performance while we periodically ran the IDS using Keyspector. In this experiment, we configured the IDS to
collect system information at intervals ranging from 0 to 20 seconds. For comparison, we measured the performance
without running the IDS.
The experiments revealed that , performance degradation was similar in the emulator and the real device and was 0.7-22%.
This overhead was reduced by lowering the frequency of the execution of the IDS.

## Slide 25: Related Work
IDS with SMM [Rutkowska+, BlackHat’08][Zhang+, DSN’13]…
  Securely execute host-based IDS by using SMM
  Not easy to update IDS embedded into BIOS
SSdetector [Koga+, TrustCom’23]
  Securely execute updatable IDS by combining Intel SGX and SMM
  Need to send heartbeats to IDS to monitor the state of IDS
Elasticlave [Yu+, Security’22]
  Allow flexible memory sharing among enclaves and the target system
  Assume that they share part of the memory
Notes: Several methods of IDS with SMM achieve the secure execution of host-based IDS by using System Management Mode.
However, it is not easy to update IDS embedded into BIOS.
Keyspector can easily update IDS running in an enclave.
SSdetector enables the secure execution of host-based IDS by combining Intel SGX and SMM.
To detect the termination of the SGX enclave running IDS by attackers, a remote host periodically sends heartbeats to IDS.
In Keyspector, the security monitor can check the execution state of IDS.
Elasticlave is a memory model that enables flexible memory sharing among enclaves and the target system in RISC-V.
It assumes that they share a part of their memory, while Keyspector shares the entire system memory with an enclave.

## Slide 26: Conclusion
We proposed Keyspector for enabling the secure execution of IDS using RISC-V Keystone
  IDS directly accesses the memory of the target system
  The security monitor limits enclaves that can share system memory
  Collect the OS data of the target system
  The overhead was 10% on a real IoT device
Future work
  Integrate controlled memory sharing with remote attestation
  Monitor the state of the enclave running IDS
  Collect other types of system information
Notes: In conclusion, we proposed Keyspector for enabling the secure execution of IDS using RISC-V Keystone.
Keyspector runs IDS in an enclave and allows it to directly access the memory of the target system.
It limits enclaves that can share the system memory.
We have developed the IDS that collects the OS data of the target system
and confirmed that the overhead was 10%.
One of our future work is to implement a mechanism for combining controlled memory sharing with remote attestation.
Also, we would like to monitor the state of the enclave running IDS in the security monitor.
We need to collect other types of system information to implement various types of IDS.