## Slide 1: Software-defined SEV for Confidential VMs Based on the Delegation Architecture in RISC-V
Junpei Matsushita and Kenichi Kourai
Kyushu Institute of Technology, Japan
Notes: I’m Kenichi Kourai from Kyushu Institute of Technology.
I’m gonna talk about Software-defined SEV for Confidential VMs Based on the Delegation Architecture in RISC-V.
This is joint work with my student.

## Slide 2: Confidential VMs (CVMs)
Users handle sensitive information in clouds
  The threat of cloud insiders is increasing
  Eavesdrop on and tamper with sensitive information in users' VMs
Recent clouds offer confidential VMs
  The memory is protected by trusted execution environments (TEEs)
  TEEs are isolated even from the hypervisor
sensitive
information
CVM
CVM
hypervisor
insider
Notes: Recently, users handle sensitive information in virtual machines [VMs] provided by cloud providers.
As a result, the threat of cloud insiders is increasing.
They can eavesdrop on sensitive data stored in users' VMs.
They can also tamper with sensitive data and the code that handles it.
To protect such sensitive information, several clouds, such as Amazon Web Services, Google Cloud, and Microsoft Azure, offer confidential VMs [CVMs].
Confidential VMs can prevent cloud insiders from eavesdropping on and tampering with sensitive data inside them.
A Confidential VM is a VM whose memory is protected using a trusted execution environment (TEE), which is provided by hardware.
A TEE is isolated even from the hypervisor.
Examples of TEEs for Confidential VMs are AMD SEV-SNP, Intel TDX, and Arm CCA.

## Slide 3: RISC-V CoVE
Confidential VM Extension (CoVE) is provided in RISC-V
  Use the trusted TEE security manager (TSM) to run CVMs
Three deployment models are defined
  Model 1: Run the TSM on confidential memory divided by hardware
  Model 2: Run the hypervisor on the TSM using nested virtualization
  Model 3: Run the TSM inside the firmware running in M-mode
hypervisor
TSM
CVM
TSM
CVM
hypervisor
firmware
CVM
TSM
model 1
model 2
model 3
VM
hypervisor
Notes: RISC-V processors also provide Confidential VM Extension (CoVE) to run Confidential VMs.
RISC-V is an open-source instruction set architecture that has recently gained attention.
CoVE uses the TEE security manager (TSM) as a part of the software TCB.
There are three deployment models in CoVE.
Model 1 runs the TSM in parallel to an untrusted hypervisor.
It divides physical memory into confidential memory assigned to Confidential VMs and non-confidential memory using additional hardware.
Model 2 runs the hypervisor on top of the TSM using nested virtualization.
It divides physical memory into confidential and non-confidential using memory virtualization.
Model 3 runs the TSM inside the firmware in the most privileged mode called M-mode.
The TSM protects the physical memory of Confidential VMs using RISC-V standard hardware.

## Slide 4: Direct Management Architecture
Use two-stage address translation to isolate CVMs
  Translate a GVA into a GPA using the VS-stage page tables (PT)
  Translate the GPA into an HPA using the G-stage PT
The two PTs are protected to guarantee its correctness
  The VS-stage PT is managed by the guest OS in a protected CVM
  The G-stage PT is managed by the trusted TSM
untrusted
hypervisor
trusted TSM
protected CVM
VS-stage PT
G-stage PT
GVA (guest virtual address)
GPA (guest physical address)
HPA (host physical address)
Notes: Each Confidential VM is isolated by using the G-stage page tables to translate a guest physical address (GPA) into a host physical address (HPA).
Address translation from a guest virtual address (GVA) into a guest physical address is performed using the VS-stage page tables in a Confidential VM.
In CoVE, the correctness of this two-stage address translation is guaranteed because both the two page tables are protected.
The VS-stage page tables are stored in the confidential memory of a Confidential VM.
They are managed by the guest OS and cannot be accessed by an untrusted hypervisor.
The G-stage page tables are stored in the protected memory of the TSM.
They are managed by the TSM and cannot be accessed by the hypervisor.
This is called the direct management architecture.

## Slide 5: AMD SEV-SNP
Use no such trusted component as the TSM
  Could reduce the TCB size
  The NPT (= G-stage PT) is managed by an untrusted hypervisor
Not guarantee the correctness of address translation
  Can change memory assignment to a CVM (remapping attack)
  Can map the same memory to multiple locations (aliasing attack)
untrusted hypervisor
protected CVM
guest PT
NPT
GVA
GPA
HPA
GPA'
HPA'
GVA'
Notes: On the other hand, AMD SEV-SNP does not use such a trusted software component as the TSM.
So, it could reduce the size of the software TCB.
However, it cannot protect the nested page tables (NPT), which correspond to the G-stage page tables in RISC-V.
Since the nested page tables are stored in the memory of an untrusted hypervisor, it can be tampered with.
This means that the correctness of two-stage address translation is not guaranteed.
For example, the hypervisor can mount memory remapping attacks, which change the assignment of physical memory to a Confidential VM so that the Confidential VM uses arbitrary code and data.
It can also mount memory aliasing attacks, which map the same physical memory to multiple locations in a Confidential VM so that the Confidential VM stores sensitive data in unintentional locations.

## Slide 6: Delegation Architecture
Use the hardware-protected Reverse Map Table (RMP)
  Maintain a reverse mapping from an HPA to a GPA
  Maintain a page owner (CVM or the hypervisor)
Perform an RMP check on every address translation
  Verify the consistency between forward and reverse mappings
  Verify the correctness of page ownership
untrusted hypervisor
CVM 1
NPT 1
RMP
GPA
HPA
GPA
HPA
GPA'
HPA'
CVM 2
NPT 2
Notes: Even in this delegation architecture, to guarantee the correctness of two-stage address translation, SEV-SNP uses the hardware-protected reverse map table (RMP).
The RMP maintains the reverse mapping from a host physical address [HPA] to a guest physical address [GPA], and a page owner, which Confidential VM or the hypervisor.
Upon memory access, it is used to verify the consistency between forward and reverse mappings.
Specifically, the processor checks that, when a guest physical address [GPA] is translated into a host physical address [HPA] using the G-stage page tables, the obtained host physical address [HPA] can be translated back into the same guest physical address [GPA] using the RMP.
The processor also verifies the correctness of page ownership.
For example, the RMP check fails when the hypervisor accesses the memory of Confidential VMs.

## Slide 7: Research Question
It is unclear whether this delegation architecture of SEV-SNP is implementable in RISC-V
Goals
  Design the delegation architecture for RISC-V
  Clarify the runtime overhead of its implementation
hypervisor
direct management architecture
delegation architecture
hypervisor
TSM
CVM
CVM
RMP
RISC-V processors
AMD processors
Notes: However, it is unclear whether this delegation architecture of SEV-SNP is implementable in RISC-V.
Our goals are to design the delegation architecture for RISC-V and to clarify the runtime overhead of its implementation.

## Slide 8: Software-defined SEV (SD-SEV)
Realize the delegation architecture mostly in software
  Use a small trusted software module (SEV module)
  Rely on a minimal hardware extension
The SEV module runs inside the firmware in M-mode
  Isolated from an untrusted hypervisor running on the firmware
  Emulate SEV-SNP features, e.g., memory integrity and authenticity
untrusted hypervisor
CVM
firmware
SEV module
M-mode
G-stage PT
VS-stage PT
Notes: We propose software-defined SEV (SD-SEV), in contrast to hardware-based SEV in AMD processors.
SD-SEV realizes the delegation architecture for Confidential VMs using a small, trusted software module called the SEV module and a minimal hardware extension.
The SEV module runs inside the firmware, which runs in the most privileged M-mode on RISC-V processors.
Therefore, the SEV module is isolated from an untrusted hypervisor running on top of the firmware and is securely executed.
It emulates the SEV-SNP features of AMD processors.
Currently, we focus on memory integrity and authenticity.

## Slide 9: Threat Model
Trust assumptions
  Software in M-mode, including the SEV module, is trusted
  The hypervisor and the G-stage PT are untrusted
Attacker model
  Remapping and aliasing attacks by modifying the G-stage PT
  Direct attacks against the memory of CVMs by the hypervisor
  Attacks against the boot images loaded into CVMs
untrusted hypervisor
CVM
trusted firmware
M-mode
G-stage PT
VS-stage PT
boot image
Notes: We assume that software running in M-mode, including the SEV module, is trusted.
We do not trust the hypervisor or the G-stage page tables it manages.
We assume attacks against two-stage address translation by modifying the G-stage page tables, for example, memory remapping and aliasing attacks.
Also, we assume that the hypervisor directly attacks the memory of Confidential VMs.
In addition, we assume attacks against the boot images loaded into Confidential VMs by the hypervisor.
However, we exclude physical attacks because it is difficult for a software-based approach to prevent such attacks.

## Slide 10: RMP Initialization
The hypervisor invokes the SEV module using an SBI call
  Instead of issuing a command of AMD Secure Processor (AMD-SP)
  Allocate and pass the memory region used for the RMP
The SEV module protects the RMP using RISC-V PMP
  Configure the memory region to be read-only for the hypervisor
  Create entries for 4-KB physical pages in the RMP
hypervisor
SEV module
RMP
SBI call
RISC-V PMP
protect
init
Notes: In hardware-based SEV, the co-processor called the AMD-SP provides the command to initialize the RMP.
In SD-SEV, the SEV module provides an SBI call for this function.
An SBI call is a mechanism to invoke the underlying software.
The hypervisor allocates the memory region used for the RMP and invokes the SEV module with it.
To prevent the hypervisor from directly modifying the RMP, the SEV module protects the passed memory region using physical memory protection (PMP) in RISC-V.
PMP is a hardware mechanism for configuring access control to physical memory regions in M-mode.
The SEV module configures the physical memory region used for the RMP to be read-only for the hypervisor.
Then, it creates entries for 4-KB physical pages in the RMP.

## Slide 11: RMP Update
The hypervisor updates an RMP entry using an SBI call
  The SEV module sets the VM ID and the GPA in the RMP entry
  It marks the RMP entry as unvalidated to delect illegal assignment
A CVM updates an RMP entry via the hypervisor
  Mark a page as unassigned to a CVM
  Share the memory accessed by virtual devices with the hypervisor
hypervisor
CVM 1
SEV module
SBI call
SBI call
RMP
update
HPA | VM ID | GPA | Assigned | Validated
10 | 1 | 50 | 1 | 0
11 | 2 | 51 | 0 | 0
CVM 2
RMP
Notes: In hardware-based SEV, the processor provides an instruction to update an RMP entry.
In SD-SEV, the SEV module provides an SBI call for this function.
The hypervisor issues this SBI call with the host physical address [HPA] of a page, the VM ID, and the assigned guest physical address [GPA].
Then, the SEV module sets the VM ID and the guest physical address [GPA] to the RMP entry corresponding to the host physical address [HPA].
At this time, it marks the RMP entry as unvalidated so that the Confidential VM can detect the illegal update of memory assignment.
When a Confidential VM shares a page to communicate with the hypervisor, it invokes the hypervisor, and then the hypervisor invokes the SEV module.
In this case, the SEV module marks the page as unassigned to a Confidential VM.

## Slide 12: Validation of an RMP Entry
A CVM validates an RMP entry by specifying a GVA
  The SEV module traps an undefined instruction used for this purpose
  It marks the RMP entry as validated to accept current assignment
The SEV module finds the RMP entry from the GVA
  Translate the GVA into an GPA using the VS-stage PT manually
  Translate the GPA into an HPA using the G-state PT manually
hypervisor
SEV module
trap
RMP
update
HPA | VM ID | GPA | Assigned | Validated
10 | 1 | 50 | 1 | 1
GVA
GPA
HPA
CVM 1
RMP
G-stage PT
VS-stage PT
Notes: In hardware-based SEV, the processor provides an instruction to validate an RMP entry to a Confidential VM.
SD-SEV uses an undefined instruction for this purpose.
The guest OS in a Confidential VM executes the undefined instruction with a guest virtual address [GVA] to be validated.
The SEV module directly traps the instruction as an exception.
It manually translates the specified guest virtual address [GVA] into a guest physical address [GPA] using the VS-stage page tables.
Then, it manually translates the obtained guest physical address [GPA] into a host physical address [HPA] using the G-stage page tables.
Finally, it marks the RMP entry corresponding to the host physical address [HPA] as validated if the VM ID and the obtained guest physical address [GPA] match the RMP entry.

## Slide 13: Extention of Page Success Exception (#PS)
#PS is a new exception added to RISC-V [Yamamoto+'25]
  Raised when the success of address translation on a TLB miss
    Opposite of the page fault exception
  The firmware can perform access control using the VA and PA
Add support for the two-stage address translation of VMs
  The SEV module performs an RMP check using the GPA and HPA
firmware
OS
process
PT
VA
PA
#PS
hypervisor
CVM
firmware
#PS
GPA
HPA
G-stage PT
VS-stage PT
GVA
Notes: It is difficult for the SEV module to efficiently perform an RMP check on every memory access.
So, SD-SEV uses a new exception added to RISC-V, called the page success exception.
A #PS exception is raised when the processor succeeds in address translation after a TLB miss.
It is the opposite of the page fault exception.
Using this exception, the firmware can perform access control using the virtual address [VA] and physical address [PA] of the accessed memory.
We extended this mechanism to add support for two-stage address translation.
A #PS exception is raised when the processor succeeds in both the VS-stage and G-stage address translations.
The SEV module can obtain the guest physical address [GPA] and host physical address [HPA] of the accessed memory.

## Slide 14: RMP Check
Verify page ownership and mapping consistency
  Find the RMP entry corresponding to the HPA
  Fail if the hypervisor attempts to access the page assigned to a CVM
  Fail if the VM ID and the GPA do not match the RMP entry
Verify page validation status
  Fail if a CVM attempts to access an unvalidated page
hypervisor
CVM 1
SEV module
#PS
RMP
check
GPA
HPA
HPA | VM ID | GPA | Assigned | Validated
10 | 1 | 50 | 1 | 1
RMP
G-stage PT
Notes: The SEV module first finds the RMP entry corresponding to the host physical address [HPA].
Then, it verifies page ownership.
When the hypervisor accesses the page assigned to a Confidential VM, the RMP check fails.
If the VM ID does not match the RMP entry, the RMP check also fails because the CVM owning that page is different.
Next, the SEV module verifies mapping consistency.
If the guest physical address [GPA] does not match the RMP entry, the RMP check fails because the reverse mapping is not consistent with the forward mapping.
Finally, the SEV module verifies validation status.
If the Confidential VM accesses unvalidated page, the RMP check fails.

## Slide 15: Measurement of a Boot Image
SD-SEV measures the initial memory pages of a CVM
  The target regions consist of a boot image including the OS
The hypervisor measures each page using an SBI call
  The SEV module updates a launch digest (LD) of the CVM
  It computes a hash value of the page, its GPA, and the current LD
  It marks the corresponding RMP entry as validated to bootstrap
hypervisor
CVM 1
SEV module
LD
SBI call
boot image
load
RMP
update
HPA | VM ID | GPA | Assigned | Validated
12 | 1 | 52 | 1 | 1
RMP
Notes: In hardware-based SEV, the AMD-SP measures the contents and metadata of the initial set of memory pages in a Confidential VM into a hash value called a launch digest.
This launch digest is used to detect an illegal modification of the boot image by the hypervisor.
In SEV-SD, the SEV module provides SBI calls for this function.
First, the hypervisor stores the boot image, such as the guest OS, in the memory of the Confidential VM.
When the hypervisor issues an SBI call to measure each page, the SEV module computes the hash value of the specified page, its guest physical address [GPA], and the current value of the launch digest, and updates the launch digest.
In addition, it marks the RMP entry corresponding to the page as validated to enable bootstrapping.

## Slide 16: LD Verification
SD-SEV can verify the LD at the boot time of a CVM
  The VM owner can pass an ID block to the SEV module
  The ID block contains the pre-computed LD of the CVM
The SEV module checks the LD on finishing measurement
  Fail if the computed LD does not match the ID block
  Detect the tampering of the boot image by the hypervisor
hypervisor
CVM
SEV module
LD
SBI call
boot image
ID block
Notes: Like hardware-based SEV, SD-SEV can optionally verify the launch digest when the measurement is finished.
The owner of the Confidential VM can pass an ID block to the SEV module via the hypervisor.
An ID block contains the value of the launch digest pre-computed by the owner.
When the hypervisor registers an ID block, the SEV module compares the computed launch digest with the pre-computed one.
If these two values are different, the SEV module detects the tampering of the boot image by the hypervisor.

## Slide 17: Experiments
We conducted several experiments
  Compare the TCB size with CoVE's
  Confirm the memory integrity and authenticity of a CVM
  Exmine the overhead of SD-SEV
 | host | emulation | VM
CPU | Intel Core i7-14700 | 4 | 2
memory | 32 GB | 4 GB | 1 GB
OS | Linux 6.14 | - | Linux 6.15
hypervisor | - | Xvisor 0.3.2 | 
firmware | - | OpenSBI 1.6 | Basic Firmware
emulator | QEMU 10.0.50 | - | -
Notes: We conducted several experiments to show the effectiveness of SD-SEV.
First, we compared the TCB size of SD-SEV with those of CoVE, which is Confidential VM Extension in RISC-V.
Next, we confirmed the integrity and authenticity of the memory of a Confidential VM using SD-SEV.
Finally, we examined the overhead of SD-SEV during and after the boot of a Confidential VM and compared the performance with that of a non-confidential VM.
We used the QEMU that emulated RISC-V processors with the #PS exception because there was no hardware that supported the #PS exception yet.
We ran a modified OpenSBI as the firmware and a modified Xvisor hypervisor.

## Slide 18: TCB Size
We measured the binary sizes of the TCB
  SD-SEV, CoVE (model 2), and CoVE (model 3)
  Compared with the original TCB (OpenSBI in M-mode)
SD-SEV's TCB is only 4% larger than the baseline
  CoVE's TCB is 2-19x larger
Chart: size (MB)
| CoVE (model 2) | CoVE (model 3) | SD-SEV
baseline (OpenSBI) | 0.11 | 0.258 | 0.261
TCB | 2.07 | 0.514 | 0.271
19x
2x
4%
TSM
OpenSBI
TSM
CoVE (model 2)
CoVE (model 3)
OpenSBI
OpenSBI
SEV module
SD-SEV
Notes: We measured the binary sizes of the TCB in CoVE model 2, model 3, and SD-SEV.
The implementation of CoVE model 1 does not exist yet.
Then, we compared them with the original TCB, which is OpenSBI running in M-mode.
This figure shows the sizes of the original firmware and the TCB for Confidential VM support.
The TCB of CoVE model 2 is 19x larger than the original firmware because it includes the hypervisor-like TSM to run Confidential VMs using nested virtualization.
The TCB of CoVE model 3 is twice as large as the original firmware because the TSM in the firmware is written in Rust.
In contrast, the TCB of SD-SEV is only 4% larger.

## Slide 19: Attack Detection
We mapped two GPAs onto the same HPA in a CVM
  Detected this attack because one GPA did not match the RMP entry
We exchanged physical pages between two CVMs
  Detected this remapping attack by verifying page ownership
We loaded a modified OS into a CVM
  Detected this attack against the boot image by LD verification
GPA 10
GPA 20
HPA 1
HPA 3
HPA | VM ID | GPA | Validated
1 | 1 | 10 | 1
2 | 2 | 30 | 1
3 | 3 | 30 | 1
RMP
VM 1
VM 2
host
host
GPA 30
HPA 2
alias
VM 3
GPA 30
remap
Notes: We examined whether SD-SEV could detect memory attacks by the hypervisor.
First, we mounted the aliasing attack by mapping two different guest physical addresses [GPA] onto the same host physical address [HPA] in a Confidential VM.
The SEV module could detect this attack because one of the guest physical addresses [GPAs] did not match the RMP entry.
Second, we mounted the remapping attack by exchanging physical pages between two Confidential VMs.
When we accessed the exchanged physical pages in the Confidential VMs, the SEV module could detect the attack because each VM accessed the page that was not owned by itself.
Third, we examined whether SD-SEV could detect tampering when a modified OS was loaded into a Confidential VM.
The SEV module could detect the modification of the boot image by using the ID block.

## Slide 20: Boot Time
The boot time of a CVM was 5.5x longer
  Increase the time of both the VM creation and the OS boot
  Enabling #PS increased the boot time significantly
RMP checks took much longer due to too many #PS
  Only 0.85 us per RMP check
Chart: time (sec)
| no SEV | SD-SEV (no #PS) | SD-SEV
VM creation | 1.23 | 2.59 | 7.1
OS boot | 1.17 | 2.34 | 6.16
5.5x
Chart: time (sec)
| 計測
measurement | 1.07
RMP update | 0.44
page validation | 2.44
RMP check | 8.34
Notes: We measured the boot time of a Confidential VM.
For comparison, we used a Confidential VM with the #PS exception disabled to examine the impact of #PS exceptions.
In addition, we measured the boot time of a normal VM.
The left-hand side figure shows the boot time of VMs.
The boot time of the Confidential VM was 5.5x longer than that of the normal VM.
The time of both the VM creation and the OS boot equally increased.
When we disabled the #PS exception, the boot time decreased significantly.
The right-hand side figure shows the breakdown of the boot time.
It took only 0.85 us per RMP check, but due to too many #PS exceptions, RMP checks took much longer in total.

## Slide 21: VM Performance
Memory access performance degraded by 25-28%
  The VM raised 50-75% of #PS
File access performance degraded by 33-40%
  The virtual device in the hypervisor raised 70-90% of #PS
Network throughput degraded by 90% due to 7x #PS
Chart: memory
| read | write
no SEV | 184 | 183
SD-SEV | 132 | 138
-28%
-25%
Chart: file
| read | write
no SEV | 1063 | 598
SD-SEV | 638 | 400
-40%
-33%
Chart: network
| Category 1
no SEV | 63.7
SD-SEV | 6.3
-90%
Notes: To examine the overhead of SD-SEV after the boot, we measured the performance of VMs.
The left-hand side figure shows the memory access performance.
The performance was degraded by 29% in reads and 25% in writes.
RMP checks are the root cause of this relatively large overhead.
This benchmark caused 50-75% of #PS exceptions inside the Confidential VM.
The middle figure shows the file access performance.
The trend was similar to the memory access performance, but the overhead was larger: 40% in reads and 33% in writes.
This is because the hypervisor emulated the virtual disk device and raised a larger number of #PS exceptions.
The right-hand side figure shows the network performance.
The performance was significantly degraded by 90%.
The reason is that too many #PS exceptions occurred inside the hypervisor to emulate two virtual network devices.

## Slide 22: Impact of #PS
We increased the minimum TLB size to reduce #PS
  Increased memory read performance by 50%
  Slightly increased file read performance by 5%
  Not effective for network throughput
Chart: memory read
| 6 | 8 | 10 | 12 | 14 | 16
throughput | 137 | 204 | 208 | 205 | 199 | 148
exceptions | 12.7 | 1.85 | 1.71 | 1.67 | 1.67 | 1.63
Chart: file read
| 6 | 8 | 10 | 12 | 14 | 16
throughput | 640 | 675 | 701 | 680 | 651 | 550
exceptions | 3.58 | 1.53 | 1.5 | 1.53 | 1.46 | 1.29
Chart: network
| 6 | 8 | 10 | 12 | 14 | 16
throughput | 6.74 | 7.05 | 6.42 | 5.59 | 1.85 | 0.21
exceptions | 150 | 146 | 144 | 136 | 62 | 17
Notes: We examined whether the reduction of #PS exceptions could improve the performance.
Since a #PS exception is raised by a TLB miss, we increased the minimum TLB size in QEMU to reduce TLB misses.
As shown in the left-hand side figure, in memory reads, when we increased the minimum TLB size, the number of #PS exceptions was reduced, and the performance was increased by 50%.
In file reads, as shown in the middle figure, the number of #PS exceptions was reduced, but the performance was increased only by 5%.
For network throughput, as shown in the right-hand side figure, the number of #PS exceptions was not reduced until the minimum TLB size became very large.
Even when the number was reduced, the network performance was decreased.
This means that reducing #PS exceptions is not always effective.

## Slide 23: Related Work
ACE [Ozga+, HASP'23]
  Guarantee exclusive memory assignment by Rust's ownership
  Fomally verify the memory safety of the core part with RefinedRust
Other commercial TEEs for CVMs
  The secure EPT is managed by the trusted TDX module in Intel TDX
  The RTT is managed by the trusted RMM in Arm CCA
AnyTEE [Cerdeira+, Access'25]
  Software-defined TEE framework with hardware virtualization
  Implementing TEEs for CVMs is future work
Notes: ACE is an implementation of CoVE model 3.
The TSM is written in Rust, and using Rust's ownership mechanism, it is guaranteed that each physical page is assigned to only one Confidential VM.
In addition, the memory safety of a core part of the implementation has formally been verified using RefinedRust.
Intel TDX uses the trusted TDX module and manages the secure extended page tables, which correspond to the G-stage page tables.
Arm CCA also uses the trusted Realm management monitor and manages the Realm translation tables securely.
These are based on the direct management architecture.
AnyTEE is a software-defined TEE framework.
It uses hardware virtualization to realize software-defined TEEs.
It supports various types of TEEs, but the implementation of TEEs for Confidential VMs is future work.

## Slide 24: Conclusion
We proposed SD-SEV for CVMs based on the delegation architecture for RISC-V
  Run the small, trusted SEV module in M-mode
  Use a minimal hardware extension called a page success exception
  The SEV module performs RMP checks using #PS
  Showed that the performance of CVMs was significantly affected
Future work
  Improve performance by reducing the overhead of #PS
Notes: In conclusion, we proposed SD-SEV, which achieves the delegation architecture of SEV-SNP using a small, trusted software module and a minimal hardware extension.
The SEV module maintains the RMP and checks the correctness of two-stage address translation using the #PS exception.
We have implemented SD-SEV and confirmed that the memory integrity and authenticity of a Confidential VM were guaranteed.
Also, we showed that the performance of a Confidential VM was significantly affected by SD-SEV.
One of our future directions is to improve the performance of SD-SEV.
In particular, it is necessary to reduce the overhead of #PS exceptions.
We are planning to extend RISC-V processors so as to perform RMP checks inside processors in a usual case.