## Slide 1: Nested SEV: Secure and Generic SEV Support for Nested Virtualization
Kazuki Takiguchi and Kenichi Kourai
Kyushu Institute of Technology, Japan
Notes: I’m Kenichi Kourai from Kyushu Institute of Technology.
I’m going to talk about Nested SEV: Secure and Generic SEV Support for Nested Virtualization.
This is joint work with my student.

## Slide 2: Confidential VMs with AMD SEV-SNP
Clouds provide confidential virtual machines (VMs)
  Protect users' sensitive information from cloud insiders
AMD SEV-SNP is often used to construct confidential VMs
  Encrypt VMs' memory transparently to prevent eavesdropping
  Protect the confidentiality and integrity of the CPU register state
  Prevent software-based integrity attacks against VMs' memory
untrusted hypervisor
confidential VM
sensitive data
VM's register
state
insider
AMD Secure Processor (AMD-SP)
AMD EPYC processors
TCB
Notes: As users deal with sensitive information in virtual machines provided by clouds, the threat from cloud insiders is growing.
To protect sensitive information in users' VMs, modern clouds offer confidential VMs based on technologies such as AMD SEV.
SEV transparently encrypts the memory of VMs and allows the memory contents to be decrypted only inside the VMs.
SEV-ES extends SEV by protecting the confidentiality and integrity of the CPU register state.
SEV-SNP further enhances protection by ensuring memory integrity and preventing software-based integrity attacks against VMs' memory.
The CPU and the AMD Secure Processor form the trusted computing base.
Using these technologies, even cloud insiders cannot eavesdrop on or tamper with sensitive information in users' VMs.

## Slide 3: Nested Virtualization
The L0 hypervisor creates L1 VMs that run L1 hypervisors
  The L1 hypervisor creates L2 VMs inside an L1 VM
E.g., virtual clouds on existing clouds
  Migratable L2 VMs on AWS spot instances [Negy+, SoCC'24]
  Secure containers on Alibaba Cloud [Huang+, SOSP'23] [Lai+, OSDI'26]
SEV support is required for L1/L2 VMs but still limited
L1 hypervisor
L0 hypervisor
L2 VM
L2 VM
L1 VM
L1 VM
Notes: On the other hand, nested virtualization enables a hypervisor to run inside a VM and create nested VMs on top of it.
A system using nested virtualization consists of three levels.
The L0 hypervisor creates L1 VMs, which run L1 hypervisors.
Then, the L1 hypervisor creates L2 VMs inside an L1 VM.
One application of nested virtualization is a virtual cloud constructed on an existing cloud.
For example, a virtual cloud can run migratable L2 VMs on AWS spot instances.
On Alibaba Cloud, secure containers created using L2 VMs run on their instances.
As in public clouds, users would expect SEV protection for L2 VMs in virtual clouds.
Virtual cloud providers would benefit from protecting the L1 VMs hosting their cloud infrastructure.
However, SEV support for nested virtualization is still limited.

## Slide 4: Previous Work
Enable SEV only for L2 VMs [Piotrowski+, Microsoft'23]
  L1 VMs are not protected by SEV
  The L1 hypervisor must trust the L0 hypervisor
Enable SEV for L1/L2 VMs with VMPLs [Ge+, CCS'22]
  Run only one L2 VM per L1 VM due to no MMU virtualization support
  The L2 VM must trust the higher-privileged L1 hypervisor
 | L1's trust | L2's trust | # of L2 VMs
MS patch | L0 | - | many
Hecate | - | L1 | 1
L1 hypervisor
L0 hypervisor
L2 VM
L2 VM
L1 VM
L1 hypervisor
L0 hypervisor
L2 VM
L1 VM
Microsoft's patch
Hecate
Notes: Microsoft's patch enables SEV for L2 VMs, but it cannot apply SEV to the L1 VM that runs L2 VMs.
Since the L1 VM is not protected, the L1 hypervisor must trust the L0 hypervisor.
This trust assumption is a fundamental limitation for virtual clouds running on untrusted public clouds.
In contrast, Hecate can apply SEV not only to L2 VMs but also to L1 VMs.
It relies on the VM Privilege levels of SEV-SNP.
It divides the guest physical address space of an L1 VM using VMPLs and runs the L1 hypervisor at the highest privilege level and an L2 VM at a lower privilege level.
Since VMPLs lack support for MMU virtualization, this system can run only one L2 VM per L1 VM.
This limitation severely restricts the applicability to virtual clouds, which need to run many L2 VMs.
In addition, since this system cannot protect the L2 VM from the L1 hypervisor, the L2 VM must trust the L1 hypervisor.

## Slide 5: Nested SEV
More secure, generic SEV support for nested virtualization
  Protect L1 VMs from an untrusted L0 hypervisor
  Run multiple SEV-enabled L2 VMs inside an SEV-enabled L1 VM
Enable an L1 hypervisor to run in an SEV-enabled L1 VM
  Keep the NPT unencrypted for shadowing by the L0 hypervisor
  Emulate VM exits by switching L1/L2 VMs with implicit register saving
 | L1's trust | L2's trust | # of L2 VMs
MS patch | L0 | - | many
Hecate | - | L1 | 1
nested SEV | - | - | many
L1 hypervisor
L2 VM
L2 VM
L1 VM
L0 hypervisor
shadow NPT
NPT
VM
exit
L1 VM's register state
L2 VM's register state
...
Notes: To provide more secure and generic SEV support for nested virtualization, we propose nested SEV.
Nested SEV protects L1 VMs from an untrusted L0 hypervisor using SEV.
It allows multiple SEV-enabled L2 VMs to run inside an SEV-enabled L1 VM without relying on VMPLs.
Nested SEV enables a hypervisor to run inside an SEV-enabled L1 VM.
This is not easy because an L1 VM's memory and register state are encrypted.
For example, the L0 hypervisor needs to virtualize the Nested Page Tables for L2 VMs.
To allow it to generate a shadow NPT, the L1 hypervisor keeps the memory used for the NPT unencrypted.
Also, the L0 hypervisor needs to emulate VM exits from an L2 VM to the L1 hypervisor.
Since it cannot access the encrypted register state, it simply switches the L2 VM to the L1 VM so that the register state is automatically saved and loaded.

## Slide 6: Two Trust Models
Both models assume an untrusted L0 hypervisor
  Enable secure virtual clouds on untrusted public clouds
Model 1: Untrusted L1 hypervisors
  SEV virtualization is provided for untrusted virtual public clouds
Model 2: Trusted L1 hypervisors
  SEV passthrough is provided for trusted virtual private clouds
 | L1's trust | L2's trust
SEV virtualization | - | -
SEV passthrough | - | L1
L1 hypervisor
L0 hypervisor
L2 VM
L2 VM
L1 VM
L1 hypervisor
L0 hypervisor
L2 VM
L2 VM
L1 VM
SEV virtualization
SEV passthrough
Notes: Nested SEV supports two trust models.
Since both models assume an untrusted L0 hypervisor, they enable secure virtual clouds on top of untrusted public clouds.
To support untrusted L1 hypervisors, nested SEV provides a mechanism called SEV virtualization.
This mechanism is used to run confidential VMs on top of untrusted virtual public clouds.
To support trusted L1 hypervisors, nested SEV provides a mechanism called SEV passthrough.
This mechanism is used to efficiently run confidential VMs on top of trusted virtual private clouds.

## Slide 7: Mechanism 1 | SEV Virtualization
Protect L2 VMs from an untrusted L1 hypervisor
  Use different SEV contexts (encryption keys) between L1/L2 VMs
  Configure shared memory as unencrypted in both L1/L2 VMs
Challenge: How to provide virtual SEV to L1 VMs securely?
  Need to virtualize SEV hardware (AMD-SP and RMP)
  Cannot emulate SEV hardware securely in an untrusted L0 hypervisor
L1 hypervisor
L0 hypervisor
L2 VM
L1 VM
AMD Secure Processor (AMD-SP)
Reverse Map Table (RMP)
bounce buffer
SEV hardware
SEV context 1
SEV context 2
SEV context
Notes: The first mechanism, SEV virtualization, protects L2 VMs from an untrusted L1 hypervisor.
This is achieved by using different SEV contexts, such as encryption keys, between L1 and L2 VMs.
As in traditional SEV, L2 VMs need to share unencrypted DMA bounce buffers with the L1 hypervisor to perform I/O.
Unlike traditional SEV, not only L2 VMs but also the L1 VM configure such memory as unencrypted.
The biggest challenge in SEV virtualization is how to provide virtual SEV to L1 VMs securely.
The L0 hypervisor needs to virtualize SEV hardware, such as the AMD Secure Processor (AMD-SP) and the Reverse Map Table (RMP).
However, it cannot emulate such SEV hardware because it is untrusted.
For example, an emulated AMD-SP cannot securely manage SEV contexts, especially encryption keys, for L2 VMs.

## Slide 8: Emulation-less Multiplexing of SEV Contexts
Multiplex SEV contexts for both L1/L2 VMs on the AMD-SP
  Do not emulate the AMD-SP in the L0 hypervisor
  Maintain the SEV contexts of L1/L2 VMs inside the physical AMD-SP
The L0 hypervisor provides a virtual AMD-SP to an L1 VM
  Forward commands for managing L2 VMs to the physical AMD-SP
  Translate the virtual ASID of an L2 VM into the real ASID
virtual
AMD-SP
physical
AMD-SP
L1 hypervisor
L0 hypervisor
L2 VM
L1 VM
L2 VM's
virtual ASID
L2 VM's real ASID
L1 VM's ASID
L1 VM's SEV context
L2 VM's SEV context
Notes: Therefore, SEV virtualization uses a technique called emulation-less multiplexing.
It multiplexes SEV contexts for both L1 and L2 VMs on the AMD-SP.
To enable this, it maintains SEV contexts for not only L1 VMs but also L2 VMs inside the physical AMD-SP by performing necessary translation.
The L0 hypervisor provides a virtual AMD-SP to an L1 VM.
When the L1 hypervisor boots an L2 VM, it issues commands to the virtual AMD-SP.
Then, the virtual AMD-SP simply forwards them to the physical AMD-SP.
At this time, it translates several parameters so that they are valid in the physical AMD-SP.
For example, it translates the L2 VM's virtual ASID into the corresponding real ASID.

## Slide 9: Emulation-less Multiplexing of Memory Assignment
Multiplex memory assignment for L1/L2 VMs on the RMP
  Maintain page ownership (guest or hypervisor) for L1/L2 VMs
  Maintain reverse mapping (HPA to ASID/GPA) for L1/L2 VMs
Accommodate three ownership types in the RMP
  Map three owners (L2, L1, and L0) on two RMP ownership states
  Translate { L2's virtual ASID, L1 GPA } to { L2's real ASID, L0 HPA }
RMP
L1 hypervisor
L0 hypervisor
L2 VM
L1 VM
HPA | owner | ASID | GPA
0 | hypervisor | - | -
1 | guest | L1's | L1's
2 | guest | L2's real | L2's
L1 GPA, L2's virtual ASID,
L2 GPA
L0 HPA,
L2's real ASID,
L2 GPA
memory assignment
(L0)
(L1)
(L2)
Notes: Similarly, SEV virtualization multiplexes memory assignment for both L1 and L2 VMs on the RMP.
The RMP is used to verify the integrity of memory assignment on address translation.
In SEV virtualization, it maintains page ownership, guest-owned and hypervisor-owned, for L2 VMs as well as L1 VMs in the RMP.
For a guest-owned page, it maintains reverse mapping, which VM and guest physical address each host physical page is assigned to.
To support both L1 and L2 VMs, SEV virtualization accommodates three ownership types, L2-owned, L1-owned, and L0-owned, in the RMP.
It maps these three on the traditional two ownership states.
An L2-owned page is registered as guest-owned, but the L2 VM's ASID and L1 physical address are translated into the real ASID and L0 physical address, respectively.
An L1-owned page is also registered as guest-owned, although it is accessible to the L1 hypervisor.

## Slide 10: Mechanism 2 | SEV Passthrough
Allow a trusted L1 hypervisor to access L2 VMs
  Use the same SEV context between L1/L2 VMs
  Keep shared memory encrypted between L1/L2 VMs
Can improve the I/O performance of L2 VMs
  Need no data copies by directly accessing encrypted buffers
  Emulate MMIO by directly accessing the encrypted register state
SEV context 1
L1 hypervisor
L0 hypervisor
L2 VM
L1 VM
buffer
L2 VM's register state
Notes: The second mechanism, SEV passthrough, allows a trusted L1 hypervisor to access its L2 VMs.
This is achieved by using the same SEV context, such as an encryption key, between L1 and L2 VMs.
As a result, the L1 hypervisor and its L2 VMs can directly share encrypted memory.
This can improve the I/O performance of L2 VMs.
In SEV, VMs need to copy data between encrypted buffers and unencrypted bounce buffers.
In SEV passthrough, L2 VMs can perform I/O directly using encrypted buffers.
Similarly, in SEV, VMs need to explicitly pass register values to the hypervisor so that the hypervisor can emulate MMIO access.
In SEV passthrough, this is not necessary because the L1 hypervisor can directly access the encrypted register state of L2 VMs.

## Slide 11: SEV Context Decoupling
Challenge: How to share an SEV context between VMs?
  The SEV context is tightly coupled with the VM in traditional SEV
Decouple the SEV context from the VM
  Achieve this by partially virtualizing SEV
  Run SEV-enabled L2 VMs without involving the AMD-SP
  Assign an L1 VM's ASID to its L2 VMs to share one SEV context
physical
AMD-SP
L1 hypervisor
L0 hypervisor
L2 VM
L1 VM
L1 VM's ASID
L1 VM's SEV context
virtual
AMD-SP
Notes: The challenge in SEV passthrough is how to share an SEV context between L1 and L2 VMs.
In traditional SEV, the SEV context is tightly coupled with the VM.
SEV passthrough decouples the SEV context from the VM.
As a result, an L1 VM and its L2 VMs can share one SEV context.
SEV passthrough achieves this SEV context decoupling by partially virtualizing SEV.
Specifically, the L1 hypervisor runs L2 VMs without involving the AMD-SP.
It assigns an L1 VM's ASID to its L2 VMs, so that the L2 VMs can use the same SEV context as the L1 VM.

## Slide 12: Exclusive GPA Assignment
Issue: Sharing an SEV context conflicts with RMP checks
  The L1 hypervisor cannot access L2 VMs' pages with different GPAs
  The L0 hypervisor can maliciously swap pages with the same GPA
The L1 hypervisor exclusively assigns pages to GPA spaces
  Guarantee that the L2 GPA of each page is identical to its L1 GPA
  Can detect page swapping because the GPA always changes
GPA1
L1 VM
L2 VM
HPA2
L0
HPA1
GPA1
GPA2
swap
physical address space
GPA1
GPA2
GPA2
L1 VM
L2 VM
HPA2
L0
HPA1
physical address space
RMP
shadow NPT
NPT
NPT
RMP
Notes: However, sharing one SEV context between L1 and L2 VMs conflicts with RMP checks.
<CLICK> When an L2 VM accesses its own page, the L2 physical address, GPA1, is translated into an L0 physical address using the shadow Nested Page Tables.
<CLICK> This result matches the reverse mapping in the RMP because that page is L2-owned.
<CLICK> When the L1 hypervisor accesses the same page, its L1 physical address, GPA2, is translated into the same L0 physical address.
<CLICK> However, this result is inconsistent with the RMP because the L1 physical address is usually different from the L2 physical address.
<CLICK> Conversely, the L0 hypervisor can maliciously swap pages that have the same guest physical address, GPA1, between L1 and L2 VMs.
<CLICK> To address these issues, the L1 hypervisor exclusively assigns memory pages across guest physical address spaces so that the L2 physical address of each page is identical to its L1 physical address.
<CLICK> As a result, the L1 hypervisor can access L2 VMs’ pages.
Page swapping causes RMP check failures because the guest physical address always changes.

## Slide 13: Experiments
We conducted several experiments using nested SEV
  Ran three L1 hypervisors (KVM, BitVisor, and Xen)
  Used three SEV variants (SEV, SEV-ES, and SEV-SNP)
We show the performance of L2 VMs on L1 KVM
  SNP-enabled L1/L2 VMs with SEV virtualization/passthrough
  SEV-disabled L1/L2 VMs
 | L0 | L1 VM | L2 VM
CPU | AMD EPYC 9334 | 12 | 6
memory | 128 GB | 16 GB | 8 GB
disk | 1.6 TB SAS SSD | 30 GB | 30 GB
NIC | Broadcom 57416 | virtio-net | virtio-net
OS/hypervisor | Linux/KVM 6.11.0 | Linux/KVM 6.11.0 | Linux/KVM 6.11.0
Notes: We conducted several experiments to examine the performance of L2 VMs in nested SEV.
We ran modified Linux/KVM as the L0 hypervisor.
In an L1 VM, we ran three L1 hypervisors: modified Linux/KVM, BitVisor, and Xen.
We used three SEV variants: SEV, SEV-ES, and SEV-SNP.
Due to time constraints, we show the results only for L2 VMs on L1 KVM with SEV-SNP.
We used SEV virtualization and SEV passthrough, and compared them with nested virtualization without SEV.

## Slide 14: Performance of L2 VMs (1/2)
VM exits incurred significant overhead
  SEV-SNP increased latency by 4x even in single-level virtualization
  Less overhead in SEV passthrough due to partially virtualizing SEV
Network throughput showed relatively large degradation
  Due to many VM exits and data copies from/to bounce buffers
Chart: VM exits
| SEV virt
no SEV | 26.9
SEV virt | 54.5
SEV pass | 42.7
Chart: network
| 1 stream
no SEV | 9.8
SEV virt | 7.7
SEV pass | 8.1
Chart: memory
no SEV | 51.8
SEV virt | 49.3
SEV pass | 49.7
1.6-2x
4-5%
17-21%
Chart: 
SEV-disabled | 0
SEV virtualization | 0
SEV passthrough | 0
Chart: 
w/o SEV | 0
SEV virtualization | 0
SEV passthrough | 0
Notes: First, we show the overhead of VM exits in the left-hand side figure.
VM exits incurred significant overhead in nested SEV.
Even in single-level virtualization, SEV-SNP increased the latency by 4x.
SEV virtualization doubled the overhead, but SEV passthrough could suppress it by partially virtualizing SEV.
As shown in the middle figure, the degradation of memory performance was only 4-5%.
But network throughput showed relatively large degradation, 17-21%, as in the right-hand side figure.
Since the L2 VM caused many VM exits by access to the virtual NIC, this performance degradation was due to the high overhead of VM exits.
For SEV virtualization, the overhead of copying data between encrypted buffers and unencrypted bounce buffers was also large.

## Slide 15: Performance of L2 VMs (2/2)
The throughput of the Web server degraded for small files
  The overhead was negligible for large files
The boot time was much longer in SEV virtualization
  Due to the large overhead of NPT virtualization without huge pages
  SEV passthrough reduced this overhead by using 1-GB huge pages
Chart: Web server
| small file | large file
no SEV | 43.4 | 8.2
SEV virt | 29.2 | 8.2
SEV pass | 30.9 | 8
Chart: kernel build
no SEV | 246
SEV virt | 277
SEV pass | 282
Chart: boot
no SEV | 14.5
SEV virt | 155.1
SEV pass | 19.2
29-33%
13-15%
11x
32%
0-2%
Chart: 
w/o SEV | 0
SEV virtualization | 0
SEV passthrough | 0
Notes: Next, we show the throughput of the Web server in the left-hand side figure.
When we requested small files, nested SEV degraded the throughput by 29-33%.
In contrast, for large files, the overhead of nested SEV was negligible.
The kernel build time showed moderate overhead, 13-15%, as in the middle figure.
Finally, we show the boot time of an L2 VM in the right-hand side figure.
SEV virtualization increased the boot time by 11x mainly due to the large overhead of the virtualization of the Nested Page Tables.
It could not assign huge pages to the L2 VM, which caused many VM exits.
In contrast, SEV passthrough could reduce this overhead to 32% by using 1-GB huge pages.
This suggests that, if we implement SEV virtualization using huge pages, this overhead would be reduced dramatically.

## Slide 16: Conclusion
We proposed nested SEV to provide more secure, generic SEV support for nested virtualization
  Support two trust models: untrusted/trusted L1 hypervisors
  Provide two mechanisms: SEV virtualization/passthrough
  Based on emulation-less multiplexing and SEV context decoupling
  The average performance degradation was 0.9-30%
Future work
  Improve the performance of nested SEV
  Extend our approach to Intel TDX
github.com/ksl-kyutech/nested-sev
Notes: In conclusion, we proposed nested SEV to provide secure and generic SEV support for nested virtualization.
Nested SEV supports two trust models depending on whether the L1 hypervisor is trusted.
To support these trust models, it provides two mechanisms: SEV virtualization and SEV passthrough.
These mechanisms are based on techniques called emulation-less multiplexing and SEV context decoupling.
We showed that the average performance degradation ranged from 0.9% to 30% across SEV variants and L1 hypervisors.
One direction for future work is to improve the performance of nested SEV.
Another is to extend our approach to Intel TDX and validate the generality of the design of nested SEV.